## Slide 1
virt-llm V1.0
A PCIe LLM accelerator simulator with queues, DMA, tensor/vector backends, and Qwen per-op execution.
PCIe endpoint
BAR0 MMIO, MSI/MSI-X, Linux driver
Command ABI
SQ/CQ descriptors, DMA buffers, completions
Compute model
Scalar, vector, tensor backend split
Qwen path
24-layer FP32 per-op smoke decode
V1.0 tag is on both repositories: supercatking/qemu and supercatking/linux
V1.0 release overview | 01

## Slide 2
virt-llm V1.0
V1.0 is an end-to-end interface milestone, not a performance simulator
PCIe device
Enumerates in Linux as a PCI endpoint with BAR0 registers and interrupt support.
BAR + IRQ
Queue ABI
Guest submits descriptors through SQ and receives status through CQ.
SQ / CQ
Backend split
Scalar dispatcher, vector helpers, and tensor backend represent accelerator blocks.
OPCODE -> backend
Qwen per-op
Qwen2.5-0.5B style graph runs through explicit hardware commands.
24 layers
Reader takeaway: V1.0 proves the contract between guest software and a simulated LLM accelerator.
V1.0 release overview | 02

## Slide 3
virt-llm V1.0
System architecture separates guest Linux, PCIe device model, and host execution
Guest Linux
/dev/virt_llm0
virt_llm_pci driver
coherent DMA buffers
freestanding test/runtime
virt-llm PCIe device
BAR0 registers
SQ/CQ engine
DMA helper calls
opcode dispatcher
IRQ completion
Host QEMU process
hw/misc/virt_llm.c
QEMU PCI DMA API
host heap temp buffers
safetensors file read
CPU implementation
MMIO kick
CQ + IRQ
device model
DMA copy
QEMU machine: riscv32 virt, Linux 6.12, -device virt-llm
V1.0 release overview | 03

## Slide 4
virt-llm V1.0
Inside the virtual accelerator: control plane, data plane, and compute backends
PCIe endpoint
BARs, device id, interrupts
BAR0 MMIO
register block, queue config
DMA engine
pci_dma_read/write
SQ / CQ
descriptor and completion rings
Scalar dispatcher
kernel ABI validation
Vector backend
RMSNorm, RoPE, ADD, SwiGLU
Tensor backend
GEMM, LM head, GQA attention
Model loader
Qwen tensor table, lazy BF16->FP32
V1.0 release overview | 04

## Slide 5
virt-llm V1.0
V1.0 models the software contract; several hardware resources are still abstracted away
Explicitly modeled
+ PCIe endpoint and BAR0 registers
+ SQ/CQ command completion flow
+ DMA read/write semantics
+ INTx, MSI, MSI-X notification
+ Scalar, vector, tensor backend routing
+ Qwen safetensors metadata and lazy weights
Not modeled in V1.0
- Device-side DDR/HBM/GDDR
- SRAM, scratchpad, tile buffers
- Tensor-core pipeline timing
- PCIe bandwidth and latency
- Asynchronous command overlap
- KV cache residency and allocator
Current activation memory is guest coherent DMA memory; op execution copies tensors into QEMU heap buffers.
V1.0 release overview | 05

## Slide 6
virt-llm V1.0
BAR0 is the control plane: identity, queue setup, interrupts, and kernel metadata
Offset
Group
Registers
0x00-0x10
Identity
MAGIC, VERSION, STATUS, FEATURES
0x14-0x24
Submit queue
Q_SIZE, Q_LO, Q_HI, Q_HEAD, Q_TAIL
0x28-0x30
Interrupt and kick
IRQ_STS, IRQ_MASK, COMMAND
0x34-0x4c
Device limits
ABI, Q_MAX, XFER_MAX, IRQ_VEC, Q_CTRL, Q_STATUS, Q_ERROR
0x50-0x60
Completion queue
CQ_SIZE, CQ_LO, CQ_HI, CQ_HEAD, CQ_TAIL
0x64-0x8c
Scalar metadata
SCALAR_STATUS, KERNEL_ID, KERNEL_OPCODE, ABI, ENTRY, SIZE, CHECKSUM
BAR0: 4 KiB little-endian MMIO
BAR1: MSI-X table/PBA
Device ID: 0x1100
Magic: LLM1
V1.0 release overview | 06

## Slide 7
virt-llm V1.0
Command submission is a ring-buffer protocol with explicit completions
1. userspace
mmap DMA buffer
2. userspace
fill tensor_req + input
3. driver
handle -> DMA addr
4. driver
write SQ desc
5. BAR0
Q_TAIL + KICK
6. QEMU
read descriptor
7. backend
execute op
8. QEMU
write output
9. QEMU
write CQ entry
10. IRQ
notify guest
11. userspace
WAIT_CQ
12. test
validate status
V1.0 release overview | 07

## Slide 8
virt-llm V1.0
Descriptor and completion entries are compact hardware-facing records
SQ descriptor
opcode: select op such as GEMM_F32
flags: READY bit and future controls
input_addr: DMA address of request/input
output_addr: DMA address of output
len: request or transfer size
status/result: device writes outcome
rsvd0: command id
rsvd1/rsvd2/rsvd3: extra DMA addrs or metadata
CQ completion
command_id: matches descriptor
opcode: completed operation
backend: DMA, VECTOR, TENSOR, SCALAR
status: COMPLETE or error
result: checksum or op-specific value
q_head: device queue progress
device executes
V1.0 release overview | 08

## Slide 9
virt-llm V1.0
GEMM shows the complete control and data path
Guest A buffer
input_dma
matrix A
Guest B buffer
input_b_dma
matrix B
QEMU heap
float/u32 *A
float/u32 *B
float/u32 *C
Tensor backend
for row
for col
for inner
sum += A * B
optional bias
Guest C buffer
output_dma
result C
pci_dma_read
pci_dma_read
ptrs
pci_dma_write
C = [[19, 22], [43, 50]]
sum(C) = 134 = 0x00000086
V1.0 release overview | 09

## Slide 10
virt-llm V1.0
Opcode routing makes backend responsibility explicit
Backend
Representative opcodes
Role
DMA
DMA_COPY, MODEL_LOAD, MODEL_QUERY
metadata movement and guest memory copy semantics
SCALAR
VEC_ADD_U32, DOT_U32, SOFTMAX_Q16, POOL_MAX_U32
kernel metadata validation plus simple kernels
VECTOR
EMBED, RMSNORM, ROPE, ADD, SWIGLU, ARGMAX
elementwise, normalization, token/vector transforms
TENSOR
GEMM, LM_HEAD, GQA_ATTENTION, CONV2D
matrix and attention style compute blocks
COMPAT
INFER_XOR
legacy smoke path for initial bring-up
The backend id is written into every CQ entry, so tests can verify the intended hardware path.
V1.0 release overview | 10

## Slide 11
virt-llm V1.0
Qwen per-op path executes the transformer graph as hardware commands
token ids
embed
RMSNorm
Q/K/V GEMM
RoPE
GQA attention
O GEMM
residual
MLP GEMMs
SwiGLU
down GEMM
LM head
argmax
24 layers | hidden 896 | heads 14 | KV heads 2 | head_dim 64 | intermediate 4864 | vocab 151936
V1.0 release overview | 11

## Slide 12
virt-llm V1.0
Run V1.0 validation and read the GEMM result as an end-to-end proof
cd /home/qemu/qemu/build
ninja qemu-system-riscv32
cd /home/qemu/linux-6.12
make ARCH=riscv CROSS_COMPILE=riscv64-linux-gnu- \
O=/home/qemu/linux-6.12-build-rv32 -j32 Image
cd /mnt/c/Users/Admin/Documents/Codex/qemu
./run_virt_llm_validation.sh
Expected GEMM line
gemm ok: m=2 n=2 k=2 checksum=0x00000086
How to read it
A and B were DMA-read from guest memory.
Tensor backend computed C.
C was DMA-written to guest output.
CQ reported COMPLETE with checksum 0x86.
Release state
QEMU tag V1.0 includes this overview document. Linux tag V1.0 points at the matching driver/UAPI/runtime state.
V1.0 release overview | 12